Pak128.Nordic

Table of Contents

## Preface
Pak128.Nordic is a pakset for Simutrans. The pakset is based on Pak128.Sweden-Ex and is planned to be a continuation of said pakset along with expanding it to the other three Nordic countries of Denmark, Finland and Norway.
This document focuses on the actual objects to be included in the pakset. Use it as a guide for technical specifications and decisions regarding scope limitations.
## General guidelines
These guidelines are common for everything in the pakset unless otherwise stated.

## Railway
This section applies to standard gauge (1435mm) railway-related vehicles and buildings unless otherwise stated.
### Tracks
Pak128.Nordic uses standard gauge (1435 mm) tracks. See “Narrow Gauge” for more information about narrow gauge railways.
There should be a representative selection of track types to choose from during the different ages. Cheap and slow tracks all the way to expensive, sturdy, and fast tracks.
### Platforms
There are three platform heights in the Nordic countries: Low, medium and high. The low and medium are used for passengers while the high platforms are used for goods.
In Pak128.Nordic we will use the medium height platforms for passengers/mail and high platforms for goods. The height differences are the height above top of rail (ATR).
Platform	ATR
Low	250 mm
Medium	580 mm
High	730 mm

The distance from track-centre to platform edge is always 1700 mm.
### Signalling
Extended uses the following signal types:
- Stop signal
- Pre-signal/distant signal/repeater signal
- Combined signal
- Choose signal
- Cab signalling
- Token block signal
Each country has its own signal system and rules. Simplification is required.
Currently there are a few Swedish signals in the pakset.
### Electrification
There are three basic types of electrification: AC, DC, and third rail. There is no practical reason to distinguish between Danish and Swedish/Norwegian AC voltages.

## Trams
Standard gauge trams
### Signalling
Same as standard gauge rail.
### Electrification
DC light rail electrification

## Narrow gauge
Different narrow gauges have been used in Scandinavia, mainly in Sweden. The most common gauges were 891mm, 1000mm, and 1067mm. They will all be treated as one “narrow gauge” for game simplification purposes.
### Platforms
There are three platform heights in the Nordic countries: Low, medium and high. The low and medium are used for passengers while the high platforms are used for goods.
In Pak128.Nordic we will use the medium height platforms for passengers/mail and high platforms for goods. The height differences are the height above top of rail (ATR).
Platform	ATR
Low	250 mm
Medium	580 mm
High	730 mm

The distance from track-centre to platform edge is always 1500 mm.
### Signalling
Same as for standard gauge.
### Electrification
Only some narrow gauge lines were electrified in Sweden. Were they only DC, or also AC?

## Roads
To be written. Including buses, trucks, roadways and required infrastructure.
### Signalling
Traffic light controlled intersections
### Electrification
Trolleybus lines were present in Scandinavia, thus trolleybus electrification is necessary.

## Water Transport
Canals were never a big part of transportation solutions in Scandinavia. Lakes and seas were widely used for transport and should be the main focus.
## Air Transport
To be written. Including aircraft, airports and required infrastructure.